DVORAK96

---------------------------------------------------------------------------
This program is free software; you can redistribute it and/or
modify it under the terms of the GNU General Public License as
published by the Free Software Foundation; either version 2 of
the License, or (at your option) any later version.

This program is distributed in the hope that it will be useful,
but WITHOUT ANY WARRANTY; without even the implied warranty of
MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE.  See the GNU
General Public License for more details.

You should have received a copy of the GNU General Public License
along with this program; if not, write to the Free Software
Foundation, Inc., 59 Temple Place - Suite 330, Boston, MA
02111-1307, USA.
---------------------------------------------------------------------------

This program translates the keycodes to change the standard
layout of the IBM keyboard to an "enhanced" layout, based on the
Dvorak-style keyboard.  To be precise, the change is:


             ` 1  2  3  4  5  6  7  8  9  0  -  =   BS
             T  q  w  e  r  t  y  u  i  o  p  [  ]   \
             CL  a  s  d  f  g  h  j  k  l  ;  ' ENTER
             SH   z  x  c  v  b  n  m  ,  .  /      SH
             CT  ALT          SP            ALT     CT

                            becomes

             ` 1  2  3  4  5  6  7  8  9  0  [  ]   BS
             T  '  ,  .  p  y  f  g  c  r  l  /  =   \
             CL  a  o  e  u  i  d  h  t  n  s  - ENTER
             SH   ;  q  j  k  x  b  m  w  v  z      SH
             CT  ALT          SP            ALT     CT

The program was inspired by a utility by Ralf Brown called
RBKEYSWP which swaps the CAPS LOCK and CTRL keys.  Many of the
techniques I have used in this program were learned perusing the
code to his utility.

This program will run on most machines using DOS (it may not work
on some older machines with old BIOSes but I have never found any
such machines).  I have used it under MS-DOS and Novell DOS and
under the Linux Dosemu, and it should work fine under OpenDOS.
It has no effect under Windows, except when running DOS under
Windows.

To load the Dvorak driver early in the boot sequence, add the
following line early in your config.sys file (presumably right
after the memory managers):

 install=dvorak.com

Alternatively, you can simply run dvorak.com from the
autoexec.bat file, or the command line.

Running the progam successively will alternately enable and
disable keyboard remapping.  This allows you to share your
computer with less enlightened people who do not yet appreciate
the advantages of Dvorak.

Dvorak96 is written completely in assembly language and follows
Ralf Brown's AMIS specification for resident programs that can be
removed out of order.  It will detect high memory when available
and automatically load itself high.  It can be removed with Ralf
Brown's generic remover program (which is part of the AMIS
library) assuming that it was loaded last or later TSR's also
follow AMIS.

This program was originally written with the A86 assembler, but
to show support for the Netwide Assemble project I have ported
the code for NASM and included both versions of the source.

---------------------------------------------------------------------------
KNOWN BUGS

The '/' key on the numeric keypad is translated to 'z' since the
program cannot distinguish its keycode from the regular '/' key.

No other bugs are known.  I have used this program on many
machines since I wrote it in 1996 and it has worked well.  I
would appreciate comments or bug reports sent to Don Bindner
<dbindner@truman.edu>.
---------------------------------------------------------------------------